## Slide 1
Beyond the GPU
Driving factors, architectures, and economics of AI hardware acceleration — a systems lecture
In-depth lecture · ~2 hours

## Slide 2
ROADMAP
Seven movements
1
Why offload
The physical driving factors.
2
Workload pressures
The measured bounds.
3
The framework
Contracts + necessity test.
4
The families
Eight contract changes.
5
Landscape
Grouped, not cataloged.
6
Substrate
Software, packaging, cost.
7
Futures
Graded by evidence.
★
Conclusions
What holds everywhere.
Beyond the GPU — 2-hour lecture
2

## Slide 3
CONCEPTS PRIMER
The hardware vocabulary, in software terms
GPU
Thousands of parallel lanes; fast on regular, batched, streamed work.
Matrix / tensor engine
A whole matrix tile per instruction; control cost amortized over many multiply-adds.
Systolic array
A grid where operands flow to neighbors — a value fetched once is reused many times.
HBM & scratchpad
Stacked DRAM for bandwidth; software-managed SRAM for reuse under compiler control.
NPU / dataflow / PIM
Blocks that change a contract: wake-scope energy, static schedule, or compute in memory.
TOPS vs contract
TOPS is a peak rating (marketing). A contract is what hardware promises software.
Beyond the GPU — 2-hour lecture
3

## Slide 4
01
Why work leaves the GPU
The physical pressures behind offload
Beyond the GPU — 2-hour lecture
4

## Slide 5
THE THESIS
Two transitions, across the whole continuum
⇒ Software succeeds until it hits a limit; each transition adds specialization rather than replacing what came before.
Beyond the GPU — 2-hour lecture
5

## Slide 6
HISTORY AS CONSTRAINTS
Why general-purpose scaling stalled
The memory wall
Compute outran memory; the question became which data is resident and reused, not raw latency.
The power wall
Frequency scaling ended; more transistors help only when software exposes parallelism.
Dark silicon
Not all transistors can switch at once in a fixed power budget — specialization does more per joule.
Data movement
Energy is dominated by moving operands, not computing on them — the recurring lever.
Beyond the GPU — 2-hour lecture
6

## Slide 7
DRIVING FACTOR
Data movement dominates energy
Compute is nearly free.
Moving operands is not.
Locality sets efficiency, not FLOPS.
⇒ Every family that follows is a different way to move less data, or move it a shorter distance.
Beyond the GPU — 2-hour lecture
7

## Slide 8
DRIVING FACTOR
Memory is a distance hierarchy
Farther = more capacity.
Also more latency and energy.
Caches help only with reuse.
⇒ 'Memory-bound' is many distinct problems — each a lever a specialized design can pull.
Beyond the GPU — 2-hour lecture
8

## Slide 9
CONCEPT
CPU and GPU spend silicon differently
CPU: latency across diverse code.
GPU: throughput across regular work.
Neither wins every phase.
⇒ Specialization narrows the job in exchange for more useful work per area and per joule.
Beyond the GPU — 2-hour lecture
9

## Slide 10
CONCEPT
The GPU efficiency envelope is real and bounded
⇒ GPUs are unbeatable inside the envelope and leak outside it — that boundary is where specialists live.
Beyond the GPU — 2-hour lecture
10

## Slide 11
02
The workload pressures
The measured bounds that reshape silicon
Beyond the GPU — 2-hour lecture
11

## Slide 12
METHOD
Signatures, not labels
⇒ Characterize each phase by its behavior — the same model is compute-, bandwidth-, and capacity-bound in one request.
Beyond the GPU — 2-hour lecture
12

## Slide 13
TWO PHASES
Prefill and decode want different machines
⇒ One pooled device compromises; phase-specialized silicon is now reaching hyperscale roadmaps.
Beyond the GPU — 2-hour lecture
13

## Slide 14
WORKED BOUND
Batch-one decode is a bandwidth wall
70B model, 8-bit, one sequence.
≈48 tokens/s ceiling on an H100.
~0.3% of matrix throughput used.
⇒ Only batching or a changed memory contract moves this — the pressure behind inference-first silicon.
Beyond the GPU — 2-hour lecture
14

## Slide 15
DRIVING FACTOR
Energy spans four orders of magnitude
Always-on: microwatts.
Cloud round-trip: watts.
Wake scope sets the cost.
⇒ Always-on features are impossible on a GPU contract — a structural bound, not an efficiency gap.
Beyond the GPU — 2-hour lecture
15

## Slide 16
DRIVING FACTOR
MoE turns compute into communication
⇒ All-to-all routing can be ~1/3 of a training step — a bound in the fabric, not the arithmetic.
Beyond the GPU — 2-hour lecture
16

## Slide 17
DRIVING FACTOR
Irregular access defeats the cache
⇒ Embeddings, gather, and graph traversal are the bound no family yet owns cleanly.
Beyond the GPU — 2-hour lecture
17

## Slide 18
THE HONEST BASELINE
Software succeeds — until it meets physics
3×
IO-aware attention throughput (FlashAttention)
2–4×
KV paging / continuous batching (vLLM)
~34%
of a training step in MoE all-to-all
<300 µW
always-on keyword spotting budget
⇒ Each gain is real and each exposes a residual bound software cannot move — that residue is the case for hardware.
Beyond the GPU — 2-hour lecture
18

## Slide 19
03
The decision framework
Contracts, and a test for when to specialize
Beyond the GPU — 2-hour lecture
19

## Slide 20
THE FRAMEWORK
Hardware defines six contracts
⇒ A signature stresses some contracts, not others — that mismatch is where a new architecture earns its place.
Beyond the GPU — 2-hour lecture
20

## Slide 21
THE NECESSITY TEST
Four conditions — all must hold
1
Residual bound
A limit remains after software has done its best.
2
Material consequence
The bound actually hurts under the deployment's objective.
3
Effective lever
Hardware changes the bound rather than relocating it.
4
Lifetime economics
Recurring benefit repays fixed cost, software, and lost flexibility.
⇒ Conditions 1–3 are the architect's analysis; condition 4 is the business case — and it decides most outcomes.
Beyond the GPU — 2-hour lecture
21

## Slide 22
THE TEST, EXECUTED
Same architecture, opposite verdicts
⇒ TPU v1 specialized; Nervana/Graphcore were right on architecture but failed condition 4; enterprise stays on GPU.
Beyond the GPU — 2-hour lecture
22

## Slide 23
GPU VS SPECIALIZATION
What the GPU absorbs — and what it cannot
⇒ Absorbable bounds join the platform; structural bounds (wake scope, determinism, near-sensor, cost floors) do not.
Beyond the GPU — 2-hour lecture
23

## Slide 24
04
The accelerator families
Eight contract changes, two organizing axes
Beyond the GPU — 2-hour lecture
24

## Slide 25
THE MAP
When uncertainty resolves × where state lives
⇒ Every family is a displacement from the CPU/GPU baseline on these two axes — no point dominates.
Beyond the GPU — 2-hour lecture
25

## Slide 26
FAMILY · MECHANISM
Systolic arrays: reuse from geometry
⇒ A value fetched once is reused across the array — memory traffic only at the edges. Absorbed by everyone, including the GPU.
Beyond the GPU — 2-hour lecture
26

## Slide 27
FAMILY · DEVICE
Tensor processors: one compiler-owned schedule
⇒ Matrix engine + software-managed SRAM. Wins dense portfolios at owner scale (TPU, Trainium, MTIA).
Beyond the GPU — 2-hour lecture
27

## Slide 28
FAMILY
Deterministic dataflow / tile processors
⇒ Schedule fixed at compile time → zero variance. Bids for latency-bounded decode and reproducible execution (Groq).
Beyond the GPU — 2-hour lecture
28

## Slide 29
FAMILY
NPUs and near-sensor engines
Power-domain-first design.
Value = wake-scope energy.
Coverage, not TOPS, decides.
⇒ The most secure beyond-GPU territory: wake scope and cost floors are structurally outside the GPU contract.
Beyond the GPU — 2-hour lecture
29

## Slide 30
FAMILY
FPGAs: flexibility after manufacturing
⇒ Two compilation speeds. Wins where post-manufacture structure is the requirement; elsewhere a staging tier to ASIC.
Beyond the GPU — 2-hour lecture
30

## Slide 31
FAMILY
Wafer-scale: state at SRAM distance
⇒ Inter-chip communication becomes on-wafer routing; model-scale state stays close. Survives on anchor tenants.
Beyond the GPU — 2-hour lecture
31

## Slide 32
FAMILY
Memory-centric / processing-in-memory
⇒ Strongest condition-3 case in the survey — gated only by the lack of a portable programming model.
Beyond the GPU — 2-hour lecture
32

## Slide 33
FAMILY · FORWARD-LOOKING
Neuromorphic: energy proportional to activity
Mechanism
Event-driven spikes; synaptic state beside the neurons; nothing switches when nothing changes.
Evidence
Research-class (TrueNorth, Loihi). Validates the energy model, not yet a mainstream workload.
Beachhead
Extreme edge: always-on sensory, reflex loops, event cameras — sparse-in-time signals.
⇒ The theoretical endpoint of wake-scope logic — a direction of development, not yet a destination.
Beyond the GPU — 2-hour lecture
33

## Slide 34
SYNTHESIS
Same families, different binding constraints
⇒ Ideas migrate both ways; implementations diverge because each deployment prices the stressors differently.
Beyond the GPU — 2-hour lecture
34

## Slide 35
05
The landscape, grouped
Read through the framework — not a product catalog
Beyond the GPU — 2-hour lecture
35

## Slide 36
GROUPED LANDSCAPE
Three groups, one deciding variable
⇒ None of the challengers failed on architecture — every trajectory was decided by condition 4.
Beyond the GPU — 2-hour lecture
36

## Slide 37
GROUP · HYPERSCALER SILICON
The TPU verdict, replicated four times
Google TPU
Seventh generation; inference-emphasized; pods of thousands.
AWS Trainium
Generally available; proprietary switch fabric; 'token economics.'
Microsoft Maia
Inference-first; large on-chip SRAM; standard Ethernet.
Meta MTIA
Recommendation-first; peer-reviewed first generation.
⇒ Every major cloud fields internal tensor processors at generation depth — the second transition as industrial fact.
Beyond the GPU — 2-hour lecture
37

## Slide 38
GROUP · GPU INCUMBENTS
The competition is a memory race
⇒ Flagships cluster on capacity and bandwidth, not FLOPS — the absorption thesis operating in public.
Beyond the GPU — 2-hour lecture
38

## Slide 39
GROUP · CHALLENGERS
The contested middle consolidates
License in
A deterministic-dataflow architecture licensed into the incumbent platform.
Anchor tenancy
Wafer-scale survives on a few enormous compute agreements, then IPO.
Acquisition
Programmable tile processors absorbed by a larger incumbent.
⇒ Condition 4 — software capital, volume, distribution — decided each, not architectural merit.
Beyond the GPU — 2-hour lecture
39

## Slide 40
GROUP · CLIENT & EDGE
The continuum's other half
AI PC
NPU + GPU under shared memory; bandwidth and coverage, not TOPS, decide.
Mobile SoC
Three wake tiers; on-device foundation models; thermal equilibrium separates the field.
Embedded / µNPU
IP-licensed; cost floor and decade lifecycle dominate.
Robotics
GPU-class perception above a deterministic control floor — flexibility wins when algorithms churn.
Automotive
Determinism and lifecycle become certification objects; supply sovereignty joins economics.
Shared taxonomy
Same families as the datacenter — different binding constraints.
Beyond the GPU — 2-hour lecture
40

## Slide 41
06
Substrate & economics
Software capital, packaging, and cost
Beyond the GPU — 2-hour lecture
41

## Slide 42
SOFTWARE ECOSYSTEM
The moat is not the kernel language
⇒ Portability efforts aimed at the kernel layer solve the cheapest part; the moat sits above and below the waist.
Beyond the GPU — 2-hour lecture
42

## Slide 43
THE PACKAGE IS THE NEW NODE
Integration is the frontier
HBM
Sets every bandwidth bound; three-vendor supply; rivals the logic die in cost share.
Packaging
Reticle limit drives 2.5D, chiplets, hybrid bonding; capacity itself gates supply.
Fabric & optics
Scale-up vs Ethernet; co-packaged optics attacks network power, not latency.
⇒ The competitive frontier moved from logic to integration — the package, the rack, the facility.
Beyond the GPU — 2-hour lecture
43

## Slide 44
ECONOMICS
The full cost stack of useful work
Every family redistributes weight.
None shrinks the stack uniformly.
Power now gates deployments.
⇒ The necessity test, in cost terms: does a redistribution lower the total for this workload at this volume?
Beyond the GPU — 2-hour lecture
44

## Slide 45
ECONOMICS
Volume decides — architecture held constant
Fixed cost ≈ software enablement.
Savings scale with volume.
Flexibility has option value.
⇒ Below the volume threshold no efficiency percentage rescues the case; above it, small percentages justify large programs.
Beyond the GPU — 2-hour lecture
45

## Slide 46
07
Futures & conclusions
Graded by evidence; what holds everywhere
Beyond the GPU — 2-hour lecture
46

## Slide 47
FUTURES
Graded by evidence class
⇒ New memories arrive before new logic; the nearest contract changes enter inside incumbent platforms, via packaging.
Beyond the GPU — 2-hour lecture
47

## Slide 48
DEMAND-SIDE WILDCARDS
What could move the bounds first
Test-time compute
Reasoning longer, not larger — deepens the decode bound, strengthens inference silicon.
Persistent-state agents
Promote state residency and freshness to first-class bounds — a possible new family.
Default sparsity
MoE and retrieval push routing and gather up the priority list.
⇒ If the signatures move, the family taxonomy should be re-derived — the method predicts its own revision.
Beyond the GPU — 2-hour lecture
48

## Slide 49
CONCLUSIONS
What holds across the whole picture
A
Software converges on physics
Both transitions are software succeeding until it exposes a hard, measurable bound.
B
Necessity is decidable
A four-condition test returns specialize / market-no / stay-on-GPU from measurable inputs.
C
Condition 4 dominates
Software capital, volume, and distribution decide outcomes more than silicon merit.
D
Families, not a successor
Each changes a contract the GPU cannot adopt without ceasing to be a GPU.
E
Bounds moved to memory & power
Capacity, bandwidth, fabric, and facility power separate contenders — not FLOPS.
F
One continuum
The same taxonomy reads microwatt silicon and megawatt pods.
Beyond the GPU — 2-hour lecture
49

## Slide 50
GUIDANCE
How to use the framework
Software architects
Design against signatures; respect batch-one; measure at the useful-result boundary; the test, not the catalog.
Platform architects
Evaluate at pod and facility; prefer consumption to ownership until volume proves otherwise; protect software seams.
Hardware selection
Signatures → software ceiling → locate the bound in the partition → weight the stack → run the test.
Beyond the GPU — 2-hour lecture
50

## Slide 51
THE ARGUMENT IN ONE SENTENCE
Software optimization succeeds until it exposes a bound; the bound is absorbed by the GPU platform, escaped by changing a contract, or lived with — and the deployment class decides which.
Everything else — signatures, contracts, families, economics — is the machinery that makes that choice decidable.
Beyond the GPU — 2-hour lecture
51